## Slide 1
MILK OF MAGNESIA
Synonym: Cream of magnesium hydroxide mixture
Milk of magnesia is a suspension having not less than 7 % w/w and not more than 8.5% w/w of magnesium hydroxide [Mg (OH)2] in purified water.
Preparation:
Light magnesium oxide is mixed with solution of sodium hydroxide to get a smooth cream. Then it is diluted with water and the suspension is poured in thin stream into a solution of magnesium sulphate stirring continuously. The precipitate is allowed to settle. Then the upper clear liquid is removed by decantation and the residue is transferred on a calico cloth for filtration. The residue is then washed with water until it becomes free from sulphate ions. The precipitate is mixed with sufficient water to get the required volume.

## Slide 2
If the preparation is done from magnesium sulphate and sodium hydroxide, then the precipitate of magnesium hydroxide is a gelatinous translucent suspension.
If magnesium oxide is used, the suspension appears white and creamy consistency.
According to I.P, 0.1 % of citric acid is added to minimize the action of glass container on milk of magnesia.
It also imparts a bitter taste. 0.5 ml of volatile oil can be used for flavouring purpose.
0.2 % methyl paraben or 0.125 % sodium benzoate are used as preservative in the preparation.
Milk of magnesia is usually dispersed in blue coloured bottles because it enhances whiteness and makes the appearance of preparation more pleasing.
Properties:
It is a white uniform suspension from which varying proportion of water may separate out on standing.
Uses: It is used as an antacid and laxative. It is also used as alkaline mouth wash.
Note: Labeling states “shake well before use

## Slide 3
SODIUM BICARBONATE:
Formula: NaHCO3
Preparation:
On a small scale,it is prepared by passing CO2 gas through a solution of sodium hydroxide.The solution is concentrated to get the product.
2NaOH+CO2 →Na2CO3 + H2O
Na2CO3+ H2O+CO2→2NaHCO3

## Slide 4
On an industrial scale, it is obtained by the solvay process. Brine solution is saturated with ammonia to remove traces of impurities like Mg and Fe. The solution is now filtered and passed through carbonating tower .In this it is allowed to come in contact with a current of CO2 and the tower is cooled to enhance precipitation. The precipitate is filtered and dried.
H2O +CO2 → H2CO3
NH3+ H2CO3 → NH4HCO3
NaCl+ NH4HCO3 → NaHCO3+NH4Cl
Properties:
It occurs as white crystalline or amorphous powder having saline taste. It is freely soluble in water but practically insoluble in alcohol. When heated to 100C it gets converted to sesquicarbonate.It gives efferevescence with acids.
Assay:
Its 1g is weighed accurately .It is dissolved in 20ml of water. Now it is titrated with 0.5N sulphuric acid using methyl orange as an indicator.
Each ml of 0.5N H2SO4≡0.042 g NaHCO3

## Slide 5
Uses:
It is used for its neutralizing properties to combat systemic acidosis. It is also used for preparing buffer solutions. Its aqueous solutions are used as local applicants for burns, insect bites. It is a constituent of efferevescent mixture.