## Slide 1: LESSON 10 MODIFIED LIMIT TEST FOR SULPHATE
Principle:
Modified limit test is performed; if the limit tests for a sample (Coloured compound) cannot be done by normal method. For example, potassium permanganate is de-colourised by boiling with ethanol, filtered to remove precipitated manganese dioxide and the filtrate is subjected to the test.
The limit test for sulphate is carried out on the basis of the reaction between barium chloride and soluble sulphates in the presence of acetic acid. Then, the comparison of the turbidity produced by a given amount of the substance is done with a standard turbidity obtained from a known amount of sulphate. The barium chloride has been replaced by barium sulphate reagent which is having barium chloride, sulphate-free alcohol, and a solution of potassium sulphate. Potassium sulphate has been added to increase the sensitivity of the test. The ionic concentrations in the reagent has been so adjusted that the solubility product of barium sulphate gets exceeded, and the very small amount of barium sulphate present in the reagent acts as a seeding agent for precipitation of barium sulphate, if sulphate be present in the substance under test. Alcohol helps to prevent super-saturation and thus produces a more uniform opalescence/turbidity. Acetic acid helps to make solution acidic and barium sulphate precipitate formed is insoluble which gives turbidity/opalescence.

## Slide 2
PROCEDURE
Preparation of Test Solution (KMnO4): Dissolve 1.5 g in 50 mL of distilled water, heat on a water-bath and add gradually 6 mL of ethanol (95%), cool, dilute to 60 mL with distilled water and filter.
Take two 50 mL Nessler Cylinders. Label one as “Test” and the other as ‘Standard’.
Test | Standard
Take 10 mL of the above test solution in Nessler cylinder. | Mix 15 mL of sulphate standard solution and 15 mL of distilled water in a Nessler cylinder
Add 0.15 mL of 5.0 M acetic acid | Add 0.15 mL of 5.0 M acetic acid
Add 2.5 mL of barium sulphate reagent | Add 2.5 mL of barium sulphate reagent
Add sufficient distilled water to produce 50 mL | Add sufficient distilled water to produce 50 Ml
Stir immediately with glass rod and allow to stand for 5 minutes protected from light | 

## Slide 3
Observation: The opalescence produce in sample solution should not be greater than standard solution. If opalescence produces in sample solution is less than the standard solution, the sample will pass the limit test for sulphates and vice-versa.

## Slide 4: Limit Test for Chlorides (Modified)
PRINCIPLE:
Modified limit test is performed; if the limit tests for a sample (Coloured compound) cannot be done by normal method. For example, potassium permanganate is de-colourised by boiling with ethanol, filtered to remove precipitated manganese dioxide and the filtrate is subjected to the test.
It is based upon the chemical reaction between silver nitrate and soluble chlorides to obtain silver chloride in presence of dilute nitric acid. The silver chloride produced in the presence of dilute nitric acid makes the test solution turbid, the extent of turbidity/opalescence depending upon the amount of chloride present in the substance is compared with a standard turbidity/opalescence produced by addition of silver nitrate to a standard solution having a known amount of chloride and the same volume of dilute nitric acid as used in the test solution. If the turbidity/opalescence from the sample has been less than the standard solution, the sample will pass the limit test and vice versa. Dilute nitric acid is used in the limit test of chloride to make solution acidic and which helps silver chloride precipitate to make solution turbid at the end of process.

## Slide 5
Procedure:
Preparation of Test Solution (KMnO4): Dissolve 1.5 g in 50 mL of distilled water, heat on a water-bath and add gradually 6 mL of ethanol (95%), cool, dilute to 60 mL with distilled water and filter.
Take two 50 mL Nessler Cylinders. Label one as “Test” and the other as ‘Standard’.
Test | Standard
Take 40 mL of the above test solution in Nessler cylinder. | Take 10 mL of chloride standard solution and 5 mL of water
Add 1.0 mL of dilute nitric acid | Add 1.0 mL of dilute nitric acid
Dilute to 50 mL with distilled water | Dilute to 50 mL with distilled water
Add 1.0 mL of 5 % AgNO3solution | Add 1.0 mL of 5% AgNO3solution
Stir immediately with glass rod and allow to stand for 5 minutes protected from light | 

## Slide 6
Observation: The opalescence produce in sample solution should not be greater than standard solution. If opalescence produces in sample solution is less than the standard solution, the sample will pass the limit test for chloride and vice-versa.